## Slide 1
Fundamentals of QGIS
A Comprehensive Overview of GIS Workflows, Spatial Analysis, and Map Production

## Slide 2
Vector Data
Represents discrete real-world features using precise geometric coordinates.
Structure: Points (cities), Lines (roads), Polygons (boundaries).
Formats: Shapefile (.shp), GeoPackage (.gpkg), KML.
Scaling: Remains sharp at any zoom level.
Raster Data
Represents continuous surfaces as a grid of cells, or pixels.
Structure: Grid where each pixel holds a numerical value.
Formats: GeoTIFF (.tif), JPEG.
Scaling: Becomes pixelated (blocky) when zoomed in closely.
GIS Foundations: Data Models

## Slide 3
What are XYZ Tiles? Web-hosted maps loaded in small image squares based on coordinates (X, Y) and zoom level (Z).
Purpose Provides vital geographic background so raw vector data does not float in an empty white canvas.
Implementation in QGIS Connect to OpenStreetMap (OSM) via the Browser panel, or add custom connections like Google Satellite imagery.
Crucial Rule: Layer Order QGIS draws from bottom to top. Basemaps must always be at the very bottom of the Layers Panel stack.
Geographic Context & Basemaps

## Slide 4
The Function
Fetches specific OpenStreetMap vector data directly into the QGIS map canvas instantly, bypassing manual downloads.
The Query
Uses Key/Value pairs to search. (e.g., Key: amenity, Value: college) within a specified town or canvas extent.
The Result
Instantly generates accurate points and polygons for features without needing external datasets.
Acquiring Vector Data: QuickOSM

## Slide 5
Clip
Acts as a cookie cutter. Extracts features from one layer based strictly on the boundaries of an overlapping layer.
Buffer
Creates a defined protective distance zone (polygon) around a point, line, or existing polygon feature.
Merge
Combines multiple separate, distinct vector layers into one single, unified layer for easier management.
Dissolve
Merges internal boundaries that share a common attribute to create a single, continuous outer boundary.
Vector Geoprocessing Tools

## Slide 6
1. Create Layer
Generate a New Shapefile Layer, specifying the geometry type (Point, Line, or Polygon).
2. Toggle Edit
Enable editing mode by clicking the Pencil icon in the Layers panel.
3. Trace Features
Use the add feature tool to manually trace shapes over a high-resolution basemap.
4. Populate Data
Open the Attribute Table to log specific names and values for the newly drawn shapes.
Manual Data Creation: Digitization

## Slide 7
Elevation Models
A Digital Elevation Model (DEM) is a raster where every single pixel stores height data above sea level.
Raster Extraction
Use the 'Clip Raster by Mask Layer' tool to isolate continuous raster data to a specific, defined vector boundary.
Terrain Analysis
Utilize raw DEMs to automatically calculate and visualize Slope, Aspect, Hillshade, and topographic Contours.
Working with Raster Data & DEMs

## Slide 8
1. Load Raster
Import an unreferenced, static image (like a scanned map) into the Georeferencer tool.
2. Add GCPs
Plot Ground Control Points matching distinct landmarks on the image to the live map canvas.
3. Configure
Open Transformation Settings, set to Linear transformation and Nearest Neighbour resampling.
4. Transform
Run the process to mathematically warp and pin the image accurately over the spatial coordinate system.
Aligning Historical Data: Georeferencing

## Slide 9
Purpose of the Composer Translating raw GIS data layers into professional, readable cartographic products for sharing.
Locking Views After drawing a map box, locking layers freezes the view, allowing you to add separate inset maps securely.
Cartographic Elements Easily add dynamic Legends, Scale Bars, and North Arrows (ensuring the arrow uses EPSG:4326 CRS).
Exporting Generate the final composed layout as a high-resolution Image or a scalable PDF.
Final Map Production: Print Layout